## Slide 1: Error Detection and Correction

## Slide 2: CRC with Polynomials
A second way of viewing the CRC process is to express all values as polynomials in a dummy variable X, with binary coefficients.
P = 11001 => X4+X3+1
The power of each term shows the position of the bit; the coefficient shows the value of the bit.

## Slide 3: Continue
The benefit is even more conspicuous when we have a polynomial such as X23+X3+1.
Here the bit pattern is 24 bits in length (three Is and twenty-one Os) while the polynomial is just three terms.
The degree of a polynomial is the highest power in the polynomial.
The degree of the polynomial X6+x+1 is 6.

## Slide 4: Continue
The degree of a polynomial is 1 less that the number of bits in the pattern.
The bit pattern in this case has 7 bits.
Multiplying a term by another term is very simple; we just add the powers.
For dividing, we just subtract the power of the second term from the power of the first.

## Slide 5: Polynomials
Commonly widely used polynomials:
CRC-12 = X12+Xll+X3+X2+X+1
CRC-16 = X16+X15+X2+1
CRC-CCIIT = X16+X12+X5+1
CRC-32 = X32+X26+X23+X22+X16+X12+Xll+X10 +X8+X7+X5+X4+X2+X+1

## Slide 6: At senders end;
Message m = X14+ X12+ X8+X7+ X5
(101000110100000)
Divisor = X5+X4+ X2+1
(110101)

## Slide 7: Continue

## Slide 8: At receivers end
Message m = X14+ X12+ X8+X7+ X5
Divisor = X5+X4+ X2+1
Remainder = X3+X2+X
m+n = X14+ X12+ X8+X7+ X5+ X3+X2+X

## Slide 9: Continue

## Slide 10: Performance of CRC
CRC can detect all single errors.
CRC can detect all double-bit errors.
CRC can detect all burst errors of less than the degree of polynomials
e.g. n=16 so it can detect all burst errors of length 15bit.
CRC detects most of the larger burst errors with a high probability. More than 15bit error
For example CRC-12 detects 99.97% of errors with a length 12 or more.
CRC gives you a very powerful technique.