## Slide 1: Error Detection and Correction

## Slide 2: Error Correction
Error correction is much more difficult than error detection.
In error detection, the receiver needs to know only that the received codeword is invalid;
In error correction the receiver needs to find (or guess) the original codeword sent.
We can say that we need more redundant bits for error correction than for error detection.

## Slide 3: Dataword & Codeword
Assume the dataword is 01.
The sender consults the table (or uses an algorithm) to create the codeword 01011.
The codeword is corrupted during transmission, and 01001 is received.
First, the receiver finds that the received codeword is not in the table.

## Slide 4: Dataword & Codeword Table
The receiver, assuming that there is only 1 bit corrupted, to guess the correct dataword.
Corrupted codeword : 01001
Dataword Codeword
00 00000
01 01011
10 10101
11 11110

## Slide 5: Continue
Comparing the received codeword with the first codeword in the table (01001 versus 00000), the receiver decides that the first codeword is not the one that was sent because there are two different bits.
By the same reasoning, the original codeword cannot be the third or fourth one in the table.
The original codeword must be the second one in the table because this is the only one that differs from the received codeword by 1 bit. The receiver replaces 01001 with 01011 and consults the table to find the dataword 01.

## Slide 6: Hamming Distance
The Hamming distance between two words (of the same size) is the number of differences between the corresponding bits.
We show the Hamming distance between two words x and y as d(x, y).
The Hamming distance can easily be found if we apply the XOR operation on the two words and count the number of Is in the result.

## Slide 7: Examples
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d (OOO, 011) is 2 because 000 XOR 011 is 011 (two Is).
2. The Hamming distance d (10101, 11110) is 3 because 10101 XOR 11110 is 01011 (three Is).

## Slide 8: Minimum Hamming Distance
The measurement that is used for designing a code is the minimum Hamming distance.
In a set of words, the minimum Hamming distance is the smallest Hamming distance between all possible pairs.
We use dmin to define the minimum Hamming distance in a coding scheme.

## Slide 9: Example
To find this value, we find the Hamming distances between all words and select the smallest one.
Find the minimum Hamming distances.
d(OOO, 011) = 2
d(Oll,110)= 2
d(OOO, 101) = 2
d(Oll, 101) = 2
The dmin in this case is 2.

## Slide 10: Example 2
Find the minimum Hamming distances.
d(OOOOO, 01011) = 3
d(01011, 10101) = 4
The dmin in this case is 3.

## Slide 11: Hamming Distance and Error
When a codeword is corrupted during transmission.
Hamming distance between the sent and received codeword's is the number of bits affected by the error.
For example, if the codeword 00000 is sent and 01101 is received, 3 bits are in error.
And the Hamming distance between the two is d(OOOOO, 01101) =3.

## Slide 12: Minimum Hamming Distance for Error Detection
If we want to be able to detect up to s errors.
If s errors occur during transmission.
The Hamming distance between the sent codeword and received codeword is s.
The minimum distance between the valid codes must be s + 1.
So that the received codeword does not match a valid codeword.