## Slide 1: Backward Error Control

## Slide 2: Backward Error Control
Model of frame transmission:
Data are sent as a sequence of frames.
Frames arrive at the same order as they are sent.
Each transmitted frame suffers an arbitrary and variable amount of delay before reception.

## Slide 3: Cont…
In addition to above, following two types of errors may occur:
Lost frame: a frame fails to arrive at the other side.
A noise burst may damage a frame to such an extent that it is not recognizable at the receiving end.
Damaged frame: a recognizable frame does arrive, but some of the bits are in error.

## Slide 4: Error Control based on
Error detection: we have already discussed.
CRC: the most powerful technique for error detection.
Positive acknowledgement: the destination returns a positive acknowledgement to successfully received error-free frames.
Retransmission after timeout: the source transmits a frame that has not been acknowledged after a predetermined amount of time.
Negative acknowledgement and retransmission: the destination returns a negative acknowledgement to frames in which an error is detected. The source retransmits such frames.

## Slide 5: Error Control Techniques
Collectively, the mechanisms are refereed to as Automatic Repeat Request (ARQ).
Objective is to turn an unreliable data link into a reliable one.
Three versions of ARQ are:
Stop-and-wait
Go-back-N
Selective-repeat

## Slide 6: Stop-and-Wait ARQ
Based on the Stop-and-wait flow control technique.
The source station transmits a single frame and then waits for an acknowledgement (ACK).
No other data frame can be sent until the destination station’s reply arrives at the source station.

## Slide 7: Cont…
To take care of lost and damaged frames, the stations are equipped with:
A timer: if no recognizable ACK is received when the timer expires at the end of the time-out interval, then the same frame is sent again.
Requires that the transmitter maintain a copy of a transmitted frame until an ACK is received for it.

## Slide 8: Cont…
The ACK frame may be damaged.
The sender will timeout and resend the same frame.
The receiver receives the same frame twice.
How to identify duplicate frames?
A modulo-2 numbering scheme is used, where frames are alternately labeled with 0 or 1, and positive acknowledgements are of the form ACK0 or ACK1.

## Slide 9: Stop-and-Wait ARQ

## Slide 10: Lost Frame

## Slide 11: Lost Acknowledgment

## Slide 12: Performance
Advantages:
The main advantage of stop-and-wait ARQ is its simplicity.
It requires minimum buffer size
Disadvantages:
Inefficient.