## Slide 1: Go-back-N ARQ

## Slide 2: Go-back-N ARQ
Based on sliding window protocol.
Basic Concept:
A station may send a series of frames sequentially up to a maximum number.
The number of unacknowledgment frames outstanding is determined by window size, using the sliding-window flow control technique.
In case of no error, the destination will acknowledge incoming frames as usual.

## Slide 3: Cont…
If the destination detects error in a frame, or it receives a frame out of order, it sends a NAK for that frame (using reject of REJ frame).
The destination will discard the frame in error and all future frames until the frame in error is correctly received.
The source station, on receiving a REJ, must retransmit the frame in error plus all succeeding frames.

## Slide 4: Frame in Error

## Slide 5: Lost or Damaged Frame

## Slide 6: Lost Acknowledgment

## Slide 7: Window size limit:
Assuming 3-bit sequence number, suppose that a station sends frame 0 and gets back an ACK1, and then sends frames 1,2,3,4,5,6,7,0 and gets another ACK1.
This might either mean that RR1 is a cumulative ACK or all 8 frames were damaged.
This ambiguity can be overcome if the maximum window size is limited to 7, i.e. for a k-bit sequence number field it is limited to 2k-1.