## Slide 1: Selective Repeat ARQ

## Slide 2: Selective Repeat ARQ
In this case, only those frames are retransmitted for which negative acknowledgement has been received, in this case negative acknowledgement called SREJ, or time out has occurred.
More efficient than Go-back-N.
Receiver requires storage buffers to contain out-of-order frames until the frame in error is correctly received.
Receiver must also have the appropriate logic circuitry needed for reinserting the frames in the correct order.
Transmitter is also more complex because it must be capable of sending frames out of sequence.

## Slide 3: Lost or damaged frame

## Slide 4: Window size limit
Consider the following scenario with k = 3, and window size of 7:
Sender sends frames 0 through 6.
Receiver sends RR7 after receiving all the 7 frames.
RR7 gets lost in transit.
Sender times out and retransmits frame 0.

## Slide 5: Continue
The receiver has already advanced its receive window to receive frames 7,0,1,2,3,4,5.
The receiver wrongly assumes that frame 7 has been lost and frame 0 is accepted as a new frame.
The problem can be alleviated by using window size of no more than half the possible sequence number.