## Slide 1: Flow and Error Control

## Slide 2: Sliding Window flow control
With the use of multiple frames for a single message the stop –and-wait protocol does not perform well.
Efficiency can be greatly improved by allowing multiple frames to be in transit at the same time.
Efficiency can also be improved by making use of the full-duplex line.

## Slide 3: Sliding Window at senders end:
To keep track of the frames, sender station sends sequentially numbered frames.
Since the sequence number to be used occupies a field in the frame, it should be of limited size.
If the header of the frame allows k bits, the sequence numbers range from 0 to 2k – 1.
Sender maintains a list of sequence numbers that it is allowed to send (sender window).
The size of the senders window is at most 2k – 1.
The sender is provided with a buffer equal to the window size.

## Slide 4: Sliding Window at receiver’s end:
Receiver also maintains window of size 1.
The receiver acknowledges a frame by sending an ACK frame that includes the sequence number of the frame expected.
This also explicitly announces that it is prepared to receive the next N frames, beginning with the number specified.
This scheme can be used to acknowledge multiple frames. It could receive frames 3,4,5 but withhold ACK until frame 5 has arrived. By returning an ACK with sequence number 6, it acknowledges frames 3,4,5 at one time.
The receiver needs a buffer of size 1.

## Slide 5: Sliding window flow control

## Slide 6: Piggybacking
If two stations exchange data, each need to maintain two windows. To save communication capacity, a technique called piggybacking is used.
Each data frame includes a field that holds the sequence number of that frame plus a field that holds the sequence number used for ACK.
If a station has an ACK but no data to send, it sends a separate ACK frame.
Frame | ACK