## Slide 1: Parameters to determine satellite’s orbit

## Slide 2: Parameters to determine satellite’s orbit
There are three parameters to determine the satellite’s path and what view it will have of Earth.
Satellite’s altitude/ height,
Eccentricity
Inclination

## Slide 3: Effect of altitude on orbits
The height of the orbit, or distance between the satellite and Earth’s surface, determines how quickly the satellite moves around the Earth.
An Earth-orbiting satellite’s motion is mostly controlled by Earth’s gravity. As satellites get closer to Earth, the pull of gravity gets stronger, and the satellite moves more quickly.
Examples include NASA’s Aqua satellite, for example, requires about 99 minutes to orbit the Earth at about 705 kilometers up, while a weather satellite about 36,000 kilometers from Earth’s surface takes 23 hours, 56 minutes, and 4 seconds to complete an orbit. At 384,403 kilometers from the center of the Earth, the Moon completes a single orbit in 28 days.

## Slide 5: Effect of eccentricity on orbits
Eccentricity refers to the shape of the orbit. A satellite with a low eccentricity orbit moves in a near circle around the Earth. An eccentric orbit is oval, with the satellite’s distance from Earth changing depending on where it is in its orbit.
The eccentricity of an orbit indicates the deviation of the orbit from a perfect circle. A circular orbit has an eccentricity of 0, while a highly eccentric orbit is closer to (but always less than) 1.

## Slide 7: Effect of Inclination on orbits
Inclination is the angle of the orbit in relation to Earth’s equator. A satellite that orbits directly above the equator has zero inclination. If a satellite orbits from the north pole to the south pole, its inclination is 90 degrees.

## Slide 8: Effect of Inclination on orbits