## Slide 1
Inclination classifications of Orbit

## Slide 2
Inclination classifications of Orbit
  Equatorial
  Polar
  Inclined

## Slide 3: Inclination classifications of Satellite Orbits
A satellite may orbit around the earth in different levels.
  Equatorial Orbits( Geostationary orbit) above Earth’s equator (i=0° to the equator)
  Polar Orbits pass over both poles (i=90° to the equator)
  Other orbits called inclined orbits (0°<i<90°)

## Slide 4: Inclination Angle

## Slide 6
The inclination of the orbit determines what parts of the Earth the satellite travels over. The path on the Earth’s surface that lies directly beneath the satellite is called the ground track of the satellite.

## Slide 7: Equatorial orbit:
This orbit has zero inclination so is an equatorial orbit (located directly above the equator). It is non-inclined orbit with respect to the equator. A satellite in equatorial orbit flies along the line of the Earth's equator.
Geostationary orbit (GEO) is the equatorial orbit. This orbit has the rotational period is equal to that of the Earth.
The satellite and the Earth move together so a GEO satellite appears as a fixed point in the sky from the Earth.
Equatorial orbits can be useful for satellites observing weather patterns, as they can monitor cloud conditions around the globe. Also can be used for TV signals.

## Slide 8: Equatorial orbit:

## Slide 9: Polar orbit
Polar Orbit is the type of LEO with a high inclination angle (close to 90 degrees). This means the satellite travels over the poles.
A satellite in this orbit flies over the earth from pole to pole. They are typically inserted at lower orbits. Many of the pictures of the earth's surface in applications such as Google Earth come from satellites in these polar orbits.

## Slide 10
Inclined orbits
An orbit whose inclination in reference to the equatorial plane is not zero degrees.
A satellite is said to reside in an inclined orbit around the Earth if the orbit shows an angle other than zero degrees with the equatorial plane. This angle is called the orbit's inclination