## Slide 1: Altitude Classification of Satellite Orbits

## Slide 2
Altitude classifications of Satellites orbits
Low Earth Orbit (LEO)
Medium Earth Orbit (MEO)
Geosynchronous Orbit (GEO)

## Slide 3
Orbits:
LEO: Low Earth Orbit.
MEO: Medium Earth Orbit
GEO: Geostationary Earth Orbit

## Slide 6: High Earth Orbit
If the satellite is in a circular orbit approximately 35,863 km above the earth's surface and rotates in the equatorial plane of the earth, it will rotate at exactly the same speed as the earth and will remain above the same spot on the equator as the earth rotates.
Because the satellite orbits at the same speed that the Earth is rotating, the satellite seems to stay in place over a single spot. This high Earth orbit is called geosynchronous.

## Slide 7: Geosynchronous orbit
A satellite in a circular geosynchronous orbit directly over the equator (eccentricity and inclination at zero) will have a geostationary orbit that does not move at all relative to the ground. It is always directly over the same place on the Earth’s surface. So, its orbital period is 24 hour.

## Slide 8: Geosynchronous orbit
Objects in Geostationary orbit revolve around the earth at the same speed as the earth rotates. This means GEO satellites remain in the same position relative to the surface of earth.
These satellites are in orbit 35,863 km above the earth’s surface along the equator.
Because of the very high altitude of their orbits, geostationary satellites may have a very wide signal footprint covering up to 42% of the Earth's surface.
Theoretically 3 geostationary satellites provides 100% earth coverage
Geostationary satellites are commonly used for communications and weather-observation.

## Slide 9: Advantages
A GEO satellite’s distance from earth gives it a large coverage area, almost a fourth of the earth’s surface.
GEO satellites have a 24 hour view of a particular area.
Three satellites can establish communication from any point to another point on the globe.
For satellite communications the advantage of the geostationary orbit is that the satellite can be accessed by means of a fixed antenna and it does not need a large steerable antenna on the ground to track the satellite for signal reception.

## Slide 10: Disadvantages
  A GEO satellite’s distance also cause it to have weak signal and time delay in the signal, which is bad for point to point communication.
  GEO satellites, centered above the equator, have difficulty broadcasting signals to near polar regions
  The solution is to for non-geostationary orbit like polar or inclined orbits.

## Slide 11: Medium Earth Orbit
Closer to the Earth, satellites in a medium Earth orbit move more quickly.
Diameter of coverage is 10,000 to 15,000 km
The orbit period is in the range off 5 to 10 hours.
Most of the satellites in medium earth orbit circle the earth at approximately 8,000 to 18,000 km above the earth in an elliptical orbit around the poles of the earth. Any orbit that circles around the poles is referred to as a 'polar orbit'.
Two medium Earth orbits are: the semi-synchronous orbit and the Molniya orbit.

## Slide 12: Semi-Synchronous orbit
The semi-synchronous orbit is a near-circular orbit (low eccentricity) 26,560 kilometers from the center of the Earth (about 20,200 kilometers above the surface). A satellite at this height takes 12 hours to complete an orbit. In 24-hours, the satellite crosses over the same two spots on the equator every day. It is the orbit used by the Global Positioning System (GPS) satellites.

## Slide 13: Molniya orbit
The second common medium Earth orbit is the Molniya orbit. Invented by the Russians.
A satellite in a Molniya orbit takes 12 hours to complete its orbit.
Like a semi-synchronous orbit, a satellite in the Molniya orbit passes over the same path every 24 hours.
This type of orbit is useful for communications in the far north or south.

## Slide 14: Low Earth Orbit
Satellites in low earth orbit (LEO) satellites complete one orbit approximately every 90 minutes at a height of between 500 and 1500 km above the earth's surface.
Its orbital period is 1.5 to 2 hour.
The diameter of coverage is about 8000 Km.
During one half of the orbit, the satellite views the daytime side of the Earth. At the pole, satellite crosses over to the nighttime side of Earth.
In a 24-hour period, polar orbiting satellites will view most of the Earth twice: once in daylight and once in darkness.

## Slide 15: LEO
Satellites in this orbital range also have a very small 'footprint'--that is, the surface of the earth that can be covered by the signal broadcast from the satellite is small. Thus, lots of satellites (35 or more) are required to make worldwide communication possible. At several million dollars per satellite, this is a very expensive satellite network to build and maintain.

## Slide 16: LEO Categories
Little LEOs
  Frequencies below 1 GHz
  5MHz of bandwidth
  Data rates up to 10 kbps
  Aimed at paging, tracking, and low-rate messaging
Big LEOs
  Frequencies above 1 GHz
  Support data rates up to a few megabits per sec
  Offer same services as little LEOs in addition to voice and positioning services

## Slide 17
The coverage region of a satellite is called its footprint. This is the region from which the satellite is visible. Three geostationary satellite footprints ensure complete coverage of the earth as shown:

## Slide 18
Geostationary satellites have permanent or 24 hour visibility. Whereas LEO & MEO satellites do not have 24 hour visibility as these satellites have smaller footprints since they are closer to the earth (low satellite height). Hence, a larger number of satellites are needed to cover the earth.

## Slide 19
Parameter | LEO | MEO | GEO
Satellite Height | 500-1500 km | 5000-18000 km | 35,800 km
Orbital Period | 10-40 minutes | 2-8 hours | 24 hours
Number of Satellites | 40-80 | 8-20 | 3
Satellite Life | Short | Long | Long
Number of Handoffs | High | Low | Least(none)
Gateway Cost | Very Expensive | Expensive | Cheap
Propagation Loss | Least | High | Highest