## Slide 1: Capacity Allocation

## Slide 2
Capacity Allocation
Allocation Strategies:
FDMA (Frequency Division Multiple Access)
TDMA (Time Division Multiple Access)
CDMA (Code Division Multiple Access)

## Slide 3: Multiple Access Techniques
Multiple access techniques are used to allow a large number of users to share the allocated spectrum(range) in the most efficient manner.
As the spectrum is limited, so the sharing is required to increase the capacity over a geographical area by allowing the available bandwidth to be used at the same time by different users.

## Slide 4: TDMA Vs FDMA Vs CDMA
There are 20 people inside a room. They want to communicate each other. Assume one to one communication. What are the methods we can follow, so that everyone can communicate each other?
FDMA: Each pair should communicate in different pitches. One pair one pitch other in some another pitch. The advantage is that, no one is wasting their time for others, but they must have the ability to speak in different pitches. It is complicated and when the number of people increases, it will become difficult to speak in different pitches.
TDMA: Each pair will get 30 seconds to communicate. All pair should wait for their turn. They can speak only when their turn comes. What is the disadvantage of the system? Others are wasting their time when a particular pair is speaking. This is equivalent to Time Division Multiple Access.
CDMA: Each pair should communicate in different languages. What is the advantage here? We are not waiting for others, ie, there is no waste of time. We can speak in the same pitch, since the language is different.

## Slide 5: TDMA Vs FDMA Vs CDMA

## Slide 6: FDMA
FDMA is the process of dividing one channel or bandwidth into multiple individual bands, each for use by a single user, the available bandwidth of the common channel is divided into bands that are separated by guard bands(to prevent station interferences). Each station is allocated a band to send its data.
Frequency band divided into small frequency channels and different channels are allocated to different users like in FM radio. Multiple users can transmit at the same time but on different frequency channels.
Each user transmits with no limitations in time, but using only a portion of the whole available frequency bandwidth.
Different users are divided in the frequency domain.

## Slide 7: FDMA

## Slide 8: FDMA Types
FAMA- Fixed Assignment Multiple Access, here frequencies are pre-allocated to users/subscribers.
DAMA- Demand Assignment Multiple Access, here frequencies are dynamically allocated based on requests.

## Slide 9: TDMA
In TDMA, the entire bandwidth is available to the user but only for a finite period of time. This technology enables different users to use one frequency at the same time.
Each user is allowed to transmit only in specified time slots with a common frequency band. Multiple users can transmit at the same frequency band at different times.
In TDMA, a set of N users share the same radio channel, but each user only uses the channel during predetermined slots. A frame consists of N slots, one for each user.
For example, you might have a data burst that takes 1 millisecond (ms) for each channel. During the first ms, the data for channel 1 is passed. During the second ms, data for channel 2 is passed, and so on until all channels are serviced and you start at channel 1 again.

## Slide 10: TDMA
Each user is allowed to transmit only within specified time intervals (Time Slots). Different users transmit in different Time Slots.
When users transmit, they occupy the whole frequency bandwidth (separation among users is performed in the time domain).

## Slide 11: TDMA

## Slide 13: CDMA
In CDMA(Code Division Multiple Access),one channel carries all transmissions at the same time and use a unique code for each transmitted signal, the receiving stations are able to differentiate between signals transmitted at the same time over the same frequency allocation.
Users may transmit at the same time using the same frequency band but using different codes so that we can decode to identify a particular user.
Each user is assigned a unique code sequence (spreading code), which it uses to encode its data signal.
The receiver, knowing the code sequence of the user, decodes the received signal and recovers the original data.

## Slide 14: CDMA

## Slide 16: Combination of TDMA+FDMA
We often use a combination of TDMA+FDMA to achieve a greater number of multiple access channels
Transmission using different frequency bands at the same time = 2 channels.
Similarly, Transmission using different time slots but same frequency band = 2 channels.
But transmission using two frequency bands and two time-slots = 4 channels.