## Slide 1: Mobile IP Terminology

## Slide 2: Home address and Care-of address
The home address is static and effectively identifies the user to the internet. TCP connections are established using the home address.
The mobile node gets a new care-of address every time it connects to a new point of attachment.
The home address is associated with the home network and the care-of address is associated with a foreign network.

## Slide 3: Home address and Care-of address
Ref: Computer Networking: A Top-Down Approach, by J.F. Kurose and K.W. Ross

## Slide 4: Foreign Network and Foreign Agent
When a mobile node moves, it first connects to a foreign agent in a foreign network.
Next, the mobile node is assigned a care-of address (an IP address) by the foreign network.
The node now registers its care-of address with the home agent.

## Slide 5: Home Network and Home Agent
The home network contains a network node called Home Agent. The home address of the mobile node is the IP address of the home agent.
The home agent is responsible for receiving all the packets sent to the mobile node when the mobile node is away.
It is the responsibility of the home agent to deliver the packets to the mobile node at its current point of attachment.

## Slide 6: Home network /Home Agent foreign network / foreign Agent
Ref: Computer Networking: A Top-Down Approach, by J.F. Kurose and K.W. Ross

## Slide 7: Correspondent Node
A correspondent node is a computer that sends packets to the mobile node. A correspondent node is typically connected to its own home network.
A correspondent node is aware of only the IP address of the mobile node in the home network of the mobile node.
Any packet from the correspondent node is delivered to the home agent.

## Slide 8: Correspondent Node
Ref: Computer Networking: A Top-Down Approach, by J.F. Kurose and K.W. Ross