## Slide 1: Mobile IP Operation

## Slide 2: A Schematic Diagram of Mobile IP
Reference: Wireless Communications and Networks, by William Stallings

## Slide 3: The Basic Mechanisms in Mobile IP
The correct functioning of mobile IP depends upon the coordination of three different activities
Discovering the care-of address of a mobile node.
Registering the care-of address with the home agent.
Tunneling of packets from the home agent to the care-of address.

## Slide 4: Discovering the care-of Address
In mobile IP, both a foreign agent and a home agent periodically broadcast agent advertisement messages.
The role of foreign and home agents have been kept similar for two reasons :
A home agent for one mobile node may act as a foreign agent for another mobile node.
A mobile node can decide whether it is in the home network or in a foreign network.

## Slide 5: Agent Advertisements
Hence, an agent advertisement has the functions :
It allows mobile nodes to discover foreign agents and get care-of addresses.
It allows the mobile node to know the services provided by the foreign agent.
It allows the mobile node to determine whether an agent is its home agent or a foreign agent.

## Slide 6: Solicitation from a Mobile Node
A mobile node can generate agent solicitation messages when it is looking for a foreign agent.
It may happen that a foreign agent has offered service, but the mobile node can no longer receive advertisements from the foreign agent.
The mobile node assumes that the foreign agent is out of range. It may contact other foreign agents whose advertisements it has received, or it may send solicitation messages.

## Slide 7: Registering the Care-of Address
When a mobile node receives a care-of address from a foreign agent, its home agent needs to be informed.
Ref: Modified from , Computer Networking: A Top-Down Approach, 5/E Copyright 1996-2009 J.F. Kurose and K.W. Ross

## Slide 8: Registering the Care-of Address
The mobile node sends a registration request to its home agent through the foreign agent who has provided the new care-of address.
When the home agent receives the request, it updates its routing table and sends a registration reply back to the foreign agent.
The mobile node starts receiving packets from its home agent once the home agent has accepted its registration request.

## Slide 9: Binding for a Mobile Node
The home agent associates the care-of address of the mobile node with its home address.
Any packet coming to the home agent will be tunneled to the mobile node in future.
The home agent also associates a registration lifetime for the mobile agent.
The three entities : home address, care-of address and registration lifetime is called a binding for the mobile node.

## Slide 10: Authentication of a Registration Request
It is extremely important to authenticate a registration request. Otherwise, a malicious node may send fake registration requests.
Each mobile node and home agent must create digital signatures that cannot be forged.
This is done by using a one-way hash algorithm over all the data in the registration request.
However, there is still a possibility of a replay attack.

## Slide 11: Delivery of Packets to the Mobile Node
When the home agent receives a packet for the mobile node, it delivers the packet to the care-of address of the mobile node.
The home agent applies a transformation on the packet so that the care-of address becomes the destination address.
A reverse transformation is applied when the packet arrives at the care-of address. It appears as if the mobile node’s home address is the destination address.

## Slide 12: Mobile IP Operation

## Slide 13: Mobile IP Operation

## Slide 14: Mobile IP Operation

## Slide 15: Mobile IP Operation

## Slide 16: Mobile IP Operation