## Slide 1: Tunneling and IP-within-IP

## Slide 2: Tunneling and IP-within-IP

## Slide 3: Tunneling and IP within IP
The transfer of the packet from the home agent to the care-of address is called tunneling.
The home agent is the source of the tunnel. The home agent inserts a new tunnel header in front of the IP header of a packet addressed to the mobile agent and received by the home agent.
The tunnel header is the care-of IP address of the mobile node. The old header is preserved as it was in the original packet.

## Slide 4: Tunneling and IP within IP
The foreign agent is the receiver of the tunnel.
When the foreign agent receives the tunneled packet, it has to delete the tunnel header to recover the original packet.
The foreign agent delivers the packet to the mobile node after removing the tunnel header.
Hence, for the mobile node, the packet looks like a normal packet exactly similar to a packet that it receives when it is connected to the home network.

## Slide 5: Communication with Correspondent Nodes
Ref: Modified from , Computer Networking: A Top-Down Approach, 5/E Copyright 1996-2009 J.F. Kurose and K.W. Ross

## Slide 6: Communication with Correspondent Nodes
The communication between the mobile node and a correspondent node is asymmetrical.
Once the mobile node knows the IP address of the correspondent node, it can send packets directly to the correspondent node.
However, the correspondent node cannot send packets directly to the care-of address of the mobile node.
The correspondent node has to send packets to the home agent.

## Slide 7: Changes in Mobile IPv6
IPv6 has many features for mobility that are not present in IPv4.
Most importantly, there is no need of a foreign agent for supporting mobility in IPv6.
A mobile node will be able to configure its own care-of address through stateless address auto configuration and neighbor discovery.
This will reduce latency and increase security in Mobile IPv6.

## Slide 8: Changes in Mobile IPv6
The tunneling mechanism for delivering packets from the home agent to the mobile node will remain similar. In particular, the details of IPv6-within-IPv6 has been already worked out.
However, one of the main changes in IPv6 will be route optimization.
When a correspondent node knows the current care-of address of a mobile node, it can send packets to the mobile node directly.

## Slide 9: Communication with Correspondent Nodes in IPv6

## Slide 10: Communication with Correspondent Nodes in IPv6

## Slide 11: Communication with Correspondent Nodes in IPv6

## Slide 12: Communication with Correspondent Nodes in IPv6

## Slide 13: Communication with Correspondent Nodes in IPv6