## Slide 1: Fading

## Slide 2: Fading
Variation in signal power over distance due to:
  Medium
  Path(s)
In fix environment
  Atmospheric conditions.. May be rain fall
In Mobile environment
  Antenna or mobile unit move relatively
  Obstacles may also change (urban and rural)

## Slide 3: Multipath Propagation
Reflection
  If the surface is larger than wavelength
  Ground reflected wave with 180° phase shift
Mobile antenna is lower than buildings
  So is multipath interference
  Reflected waves may interfere constructively or destructively

## Slide 4: Diffraction
On the edges of impenetrable bodies
The obstacle may be larger than wavelength of radio waves
Propagation in different directions from these edges

## Slide 5: Scattering
Obstacle is of order of wavelength
Or less than wavelength
Signal scattering in different directions
Signals are weaker
Many small obstacles can cause scattering
  So is unpredictable

## Slide 6: Effects
Performance is affected on the basis of
  Local conditions
  Mobility
For clear LOS
  Minor Diffraction and Scattering
  Reflection may occur
When not in LOS
  Diffraction and Scattering may be major sources of fading
Multiple copies of signal received
If joined destructively
  Signal level relative to noise decreases
  Difficulty in signal detection at receiver

## Slide 7
Ref: Google Images

## Slide 8: Types of Fading
Fast fading
  Rapid variation of signal strength over a distance one half of wavelength
  Not only in automobiles but also on walking
Slow fading
  Over a long distance
  Multiples of wavelength

## Slide 9: Types of Fading …
Flat Fading
  Non selective
  All frequency components fluctuate in same proportion, simultaneously
Selective Fading
  Different components- different effects
  Attenuation over a portion of bandwidth