## Slide 1: Signal Encoding Basics and Criteria

## Slide 2: Encoding and Modulation Techniques
(Ref: Wireless Communications and Networks; 2nd Edition by William Stallings)

## Slide 3: Wireless Communication
Digital-to-analog: Digital data and signals must be converted to analog signals for wireless transmission.
Analog-to-analog: Typically, a baseband analog signal, such as voice or video, must be modulated onto a higher-frequency carrier for transmission.
Analog-to-digital: It is common to digitize voice signals before transmission to improve quality. The resulting digital data must be modulated onto an analog carrier.

## Slide 4: Key Terms
Data (bit) Rate: The number of bits per second
Baud (signaling/modulation) rate: The number of signal elements per second
Signal Element: The part of a signal that occupies the shortest interval of a signaling code
  Digital: A voltage pulse of constant amplitude
  Analog: A pulse of constant frequency, phase, and amplitude

## Slide 5: Factors Used to Compare Encoding Schemes
Signal spectrum
  With lack of high-frequency components, less bandwidth required
  With no dc component, ac coupling via transformer possible
  Transfer function of a channel is worse near band edges
Clocking
  Ease of determining beginning and end of each bit position
Signal interference and noise immunity
  Performance in the presence of noise
Cost and complexity
  The higher the signal rate to achieve a given data rate, the greater the cost

## Slide 6: Reference
Wireless Communications and Networks, 2nd Edition, by William Stallings