## Slide 1: Spread Spectrum

## Slide 2: Spread Spectrum
Important encoding method for wireless communications
Analog & digital data is encoded with analog signal
Spreads data over wide bandwidth
Makes jamming and interception harder
Two approaches, both in use:
  Frequency Hopping
  Direct Sequence

## Slide 3: Spread Spectrum
Input is fed into a channel encoder
  Produces analog signal with narrow bandwidth
Signal is further modulated using sequence of digits
  Spreading code or spreading sequence
  Generated by pseudonoise, or pseudo-random number generator
Effect of modulation is to increase bandwidth of signal to be transmitted

## Slide 4: Spread Spectrum
On receiving end, digit sequence is used to demodulate the spread spectrum signal
Signal is fed into a channel decoder to recover data

## Slide 5: Spread Spectrum

## Slide 6: Spread Spectrum
What can be gained from apparent waste of spectrum?
  Immunity from various kinds of noise and multipath distortion
    Anti-jamming performance
    Interference immunity
  Can be used for hiding and encrypting signals
    Low probability of intercept
    Low transmit power density
  Several users can independently use the same higher bandwidth with very little interference
    Multiple access communications
    Multiple simultaneous transmissions