## Slide 1: Frequency Hoping Spread Spectrum (FHSS)

## Slide 2: Frequency Hoping Spread Spectrum (FHSS)
Signal is broadcast over seemingly random series of radio frequencies
  A number of channels allocated for the FH signal
  Width of each channel corresponds to bandwidth of input signal
Signal hops from frequency to frequency at fixed intervals
  Transmitter operates in one channel at a time
  Bits are transmitted using some encoding scheme
  At each successive interval, a new carrier frequency is selected

## Slide 3: Frequency Hoping Spread Spectrum
Channel sequence dictated by spreading code
Receiver, hopping between frequencies in synchronization with transmitter, picks up message
Advantages
  Eavesdroppers hear only unintelligible blips
  Attempts to jam signal on one frequency succeed only at knocking out a few bits

## Slide 4: Frequency Hoping Spread Spectrum

## Slide 5
Frequency Hoping Spread Spectrum

## Slide 6: Frequency Hoping Spread Spectrum

## Slide 7: Frequency Hoping Spread Spectrum
Binary data are fed into a modulator using digital-to-analog encoding scheme, such as frequency-shift keying (FSK) or binary phase-shift keying (BPSK)
The resulting signal Sd(t) is centered on some base frequency.
A pseudonoise (PN), or pseudorandom number, source serves as an index into a table of frequencies, this is called the spreading code.
Each successive interval (each k PN bits), a new carrier frequency c(t) is selected.

## Slide 8: Frequency Hoping Spread Spectrum
This frequency is then modulated by the signal produced from the initial modulator to produce a new signal s(t) with carrier frequency.
At Receiver end, the spread spectrum signal is demodulated
Same sequence of PN-derived frequencies are used and then demodulate to produce the output data.

## Slide 9: FHSS Using MFSK
MFSK signal is translated to a new frequency every Tc seconds by modulating the MFSK signal with the FHSS carrier signal
For data rate of R:
  duration of a bit: T = 1/R seconds
  duration of signal element: Ts = LT seconds
Tc  Ts - slow-frequency-hop spread spectrum
Tc < Ts - fast-frequency-hop spread spectrum