## Slide 1: Direct Sequence Spread Spectrum (DSSS)

## Slide 2: Direct Sequence Spread Spectrum (DSSS)
Each bit in original signal is represented by multiple bits in the transmitted signal
Spreading code spreads signal across a wider frequency band
  Spread is in direct proportion to number of bits used
  10-bit spreading code => 10 times > bandwidth
One technique combines digital information stream with the spreading code bit stream using exclusive-OR (XOR)
  input 0: spreading code unchanged
  input 1: spreading code inverted

## Slide 3: Direct Sequence Spread Spectrum (DSSS)

## Slide 4: DSSS Using BPSK
Multiply BPSK signal,
  sd(t) = A d(t) cos(2 fct)
by c(t) [takes values +1, -1] to get
  s(t) = A d(t)c(t) cos(2 fct)
    A = amplitude of signal
    fc = carrier frequency
    d(t) = discrete function [+1, -1]
At receiver, incoming signal multiplied by c(t)
  Since, c(t) x c(t) = 1, incoming signal is recovered

## Slide 5: DSSS Using BPSK

## Slide 6: DSSS Using BPSK
Perform the BPSK modulation on the data stream d(t) to generate the data signal Sd(t).
This signal can then be multiplied by c(t)
An implementation using this interpretation is shown in above figure

## Slide 7: DSSS Example Using BPSK

## Slide 8: DSSS Performance Considerations
Gain in signal to noise ratio
Gp = Tb/ Tc ≈ Ws/ Wd
  Ws = FHSS spread spectrum signal bandwidth
  Wd = signal bandwidth
  Tb = duration of 1 bit of input signal
  Tc = duration of 1 bit of spreading code
Jamming resistance very close to FHSS
Reduced signal/background-noise level hampers interception