## Slide 1: Maximal-Length Sequences (M-Sequences)

## Slide 2: Maximal-Length Sequences (M-Sequences)
Generated using linear feedback shift-register and exclusive OR-gate circuits.
M-Sequence is a type of pseudorandom binary sequence.
M-sequences are used as a basis for deriving pseudo-random sequences in digital communication systems that employ direct-sequence spread spectrum (DSSS) and frequency-hopping spread spectrum ( FHSS) transmission systems

## Slide 3: M-Sequences
For any given size of LFSR, a number of different unique m-sequences can be generated
Generator polynomial P(X) is used to find the sequence generated by the corresponding LFSR, by taking the reciprocal of the polynomial
  P(X) = Ao + A1X + A2X2 + ... + An_1Xn- 1 + xn
Example: for 3bit LFSR with
  P(X) = 1 + X + X3 N=2n -1
Perform the division 1/(1 + X + X3 )
The result is
  1 + X + X2 + (0 ×X3) + X4+ (0 ×X5) + (0 ×X6)
The shift register output is 1110100
The period of this sequence is 7 = 23 - 1

## Slide 4: Properties of M-Sequences
Property 1:
  Has 2n-1 ones and 2n-1-1 zeros
Property 2:
  For a window of length n slide along output for N (=2n-1) shifts, each n-tuple appears once, except for the all zeros sequence
Property 3:
  Sequence contains one run of ones, length n
  One run of zeros, length n-1
  One run of ones and one run of zeros, length n-2
  Two runs of ones and two runs of zeros, length n-3
  2n-3 runs of ones and 2n-3 runs of zeros, length 1

## Slide 5: Properties of M-Sequences
Property 4:
  The periodic autocorrelation of a ±1 m-sequence is