## Slide 1: Linear Feedback Shift Register

## Slide 2: Linear Feedback Shift Register
A linear-feedback shift register (LFSR) is a shift register whose input bit is a linear function of its previous state
A circuit consisting of XOR gates and a shift register, called a linear feedback shift register (LFSR)
It is a 1-bit storage device, and each device has
  Output line: which indicates the value currently stored
  Input line: At discrete time instants, known as clock times, the value in the storage device is replaced by the value indicated by its input line

## Slide 3
The circuit is implemented as follows:
The LFSR contains n bits
There are from 1 to (n - 1) XOR gates
The presence or absence of a gate corresponds to the presence or absence of a term in the generator polynomial, P(X),
Generator as implementing a sum of XOR terms
Figure 7.12 illustrates this equation.
Linear Feedback Shift Register Implementation

## Slide 4: Linear Feedback Shift Register Implementation

## Slide 5
The output of an LFSR is periodic with maximum period N = 2n - 1.
No feedback ( all Zeros)
  If initial contents or coefficients of the LFSR are all zeros
A feedback configuration gives a Period of N,
  Resulting sequence is called m-sequences ( maximal-length sequences)

## Slide 6: Advantages of Linear Feedback Shift Register
The sequences generated by an LFSR can be nearly random with long periods, which aids in making the spread signal appear noise like
LFSRs are easy to implement in hardware
Run at high speeds, this is important because the spreading rate is higher than the data rate.