## Slide 1: Error Detection and Correction

## Slide 2: Checksum
Use to send block of data
The data is divided into k segments each of m bits.
The segments are added using one complement arithmetic to get the sum.
The sum is complemented to get the checksum.
The checksum segment is sent along with the data segments.

## Slide 3: Example
We have 32 bits of data we divide it into 4 segment each of 8bits.
11100101 00101101 11010100 10010011
Segment K=4
Message = 8
11100101
00101101
11010100
10010011

## Slide 4: At senders end:
11100101 1st segment
00101101 2nd segment
00010010
1 Carry added
00010011
11010100 3rd segment
11100111
10010011 4th segment
01111010
1 Carry added
01111011 Sum
10000100 Checksum

## Slide 5: Continue…
All received segments are added using one complement arithmetic to get the sum.
The sum is complemented.
If the result is zero, the data is accepted; otherwise rejected.

## Slide 6: At receivers end:
11100101 1st segment
00101101 2nd segment
00010010
1 Carry added
00010011
11010100 3rd segment
11100111
10010011 4th segment
01111010
1 Carry added
01111011 Sum
10000100 Checksum
11111111
00000000 Complemented

## Slide 7: Performance
The checksum detects all errors involving an odd number of bits.
It also detects most errors involving even number of bits.
Performance of checksum is comparable to that of two dimensional parity check.
Overhead 32+8=40
Less than two dimensional parity check.